## Slide 1: One layout for every kernel: NCHW8c + halo
ONNX NCHW: channel planes one after another
c0p0
c0p1
c0p2
c0p3
c1p0
c1p1
c1p2
c1p3
c2p0
c2p1
c2p2
c2p3
c3p0
c3p1
c3p2
c3p3
pixel p0's channels are H×W floats apart: 8 loads to fill one register
NCHW8c: [N][C/8][H+2][W+2][8], 8 channels of a pixel together
p0c0
p0c1
p0c2
p0c3
p0c4
p0c5
p0c6
p0c7
p1c0
p1c1
p1c2
p1c3
p1c4
p1c5
p1c6
p1c7
8 contiguous floats = 32 bytes = one _mm256_load_ps = one YMM register
Weights, packed once offline: [K/8][C/8][R][S][8 in][8 out]
Same format for 3×3 and 1×1 (R = S = 1). The 8 output-channel weights of one input channel and tap are one aligned load, read front to back. BatchNorm is folded into weights and bias.
Zero halo: padding stored
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
grey: stored zeros, 1 pixel wide
amber: a 3×3 window at the corner reads zeros, no if-statement
teal: interior, the only part a kernel writes
Notes: All three of our kernels, stride 1, stride 2 and 1 by 1, read and write the same layout, defined once in include/common.h. ONNX stores NCHW: all of channel 0, then all of channel 1, so the 8 channels of one pixel are H times W floats apart and filling one register takes 8 loads. We store NCHW8c: channels in blocks of 8, and the 8 channels of a pixel are 32 contiguous bytes, one aligned load into one YMM register. Around every plane we store a 1-pixel border of zeros, the convolution's padding written out, so a 3 by 3 window at the edge just reads zeros. Weights are packed once offline, with BatchNorm already folded in, so the 8 output-channel weights for one input channel and tap are one aligned load. Because every layer uses the same layout, layers chain with no conversion; we convert only at the network input and output, outside the timing.

## Slide 2: Does it suit every kernel? Mostly, with two costs
Kernel | Fit | Why | Cost or open question
3×3 stride 1 (Om) | Strong | 8 output channels = 1 load; 1 broadcast feeds 2 FMAs; halo: no edge branches | None found
1×1 (Simon) | Strong | Matrix multiply over channels: same broadcast-input, vector-output pattern | Halo is unused: memory, and skipping the border
3×3 stride 2 (O'Malley) | Open | Same loads and halo as stride 1 | Every other pixel per tap = half a cache line; all columns across 3 taps. Even/odd split untested
SPPF max-pool (Simon) | Own buffers | 8 channels per register: one vector max per 8 channels | Needs a 2-pixel −∞ border, not 1-pixel zeros
Shared win: no conversion between layers. C2f's Split is a pointer offset (each 8-channel block is its own plane), and Concat is the producer writing into its slice.
Notes: We chose one layout for the whole network. Here is how it fits each kernel, and to be clear, this is reasoning about each kernel's loads; we have not benchmarked an alternative layout for any of them. Stride 1: close to required. The 2 by 5 tile needs 8 output channels per register and one broadcast input per pair of FMAs; NCHW8c makes each a single load and the halo makes every call identical. 1 by 1: fits just as well, it is a matrix multiply over channels with the same broadcast-input, vector-output pattern. But it never reads a neighbour, so the halo is pure overhead for it: memory, and skipping the border while walking a row. Stride 2: open question. Within one tap it reads every other pixel, so half of each 64-byte cache line, but across the 3 horizontal taps it reads every column, so the lines are probably fully used over the window. SPPF: its max-pool needs a 2-pixel border of minus infinity, not zeros, so it needs its own buffers.

## Slide 3: Where it costs us, and what we have not measured
model.0: 3 input channels padded to 8
2.7×
the useful work
RGB input, C = 3 → one block of 8: 5 of 8 FMAs multiply zeros. One of O'Malley's 7 stride-2 layers (88.5 MFLOPs). Fix: a first-layer kernel or layout.
Halo memory: (H+2)(W+2) / HW
Plane | 160×160 | 80×80 | 40×40 | 20×20
Extra memory | +2.5% | +5.1% | +10.3% | +21%
Not measured yet
What we claim: the layout suits every kernel's loads and removes conversions between layers.
What we have not done: timed any kernel on a second layout.
Next experiments:
1. 2×5 stride-1 kernel: plain NCHW vs NCHW8c on a few layers
2. Stride 2: even/odd column split vs NCHW8c
3. A model.0 kernel that does not pad C = 3 to 8
4. 1×1: output without a halo when the next layer is 1×1
Notes: Two real costs. First, the first layer, model.0, has only 3 input channels, the RGB image. NCHW8c rounds that up to one block of 8, so 5 of every 8 multiply-adds in that layer are on zeros: the kernel does 2.7 times the useful work. The usual fix is a special first-layer kernel or layout. Second, the halo's memory: 2.5 percent at 160 by 160, but 21 percent at 20 by 20, where the border is a big share of a small plane. And to be honest about the evidence: we picked this layout for the microkernels' loads and to avoid conversions, but we have not timed any kernel on a second layout. The cheapest experiment is the 2 by 5 stride-1 kernel on plain NCHW against NCHW8c on a few layers; then an even/odd column split for stride 2.